## Slide 1: LOW COST SENSOR WITH LORACONNECTIVITY AND CALIBRATION FOR AIR POLLUTION MONITORING

## Slide 2: ABSTRACT:
Air pollution poses significant risk to environment and health. Air quality monitoring stations are often confined to a small number of locations due to the high cost of the monitoring equipment. They provide a low fidelity picture of the air quality in the city; local variations are overlooked. However, recent developments in low-cost sensor technology and wireless communication systems like Internet of Things (IoT) provide an opportunity to use arrayed sensor networks to measure air pollution, in real time, at a large number of locations. This article reports the development of a novel low-cost sensor node that utilizes cost-effective electrochemical sensors to measure carbon levels. The node can be powered by either solar-recharged battery or mains supply. It is capable of long-range, low power communication over public or private long-range wide area network IoT network and short-range high data rate communication over Wi-Fi. The developed sensor nodes were co-located with an accurate reference CO2 sensor for field calibration.
.

## Slide 3: SCOPE OF THE PROJECT:
The scope of the project presents an prototype that reports the development of a novel low-cost sensor node that utilizes cost-effective electrochemical sensors to measure carbon levels.

## Slide 4: LITERATURE SURVEY:
TITTLE 1: Convolution Recurrent Neural Networks Based Dynamic Transboundary Air Pollution Predictiona
AUTHOR Peijiang Zhao ,Koji Zettsu
YEAR: 2019
DESCRIPTION:
Transboundary air pollution is one of the main sources of air pollution in island cities. However, the transboundary pollution confounded by local emission, meteorological conditions, and it is difficult to predict. Currently, most of urban airpollution prediction methods do not predict with transboundary air pollution. Therefore, we introduce a dynamic transboundary air pollution prediction approach based on convolutional recurrent neural networks(D-CRNN) which: (i) Divide the prediction inputs into prediction locations and transboundary air pollution sources; (ii) Use two different convolutional recurrent neural networks to solve the spatial-temporal feature of each inputs. (iii) Through a transboundary prediction network to integrate the spatial-temporal feature of prediction locations with the spatial-temporal feature of transboundary air pollution sources in a dynamic asynchronous method. Then use those mixed features to predict the air pollution. We evaluate our DCRNN model with the local atmospheric monitoring data in Kyushu, Japan and the transboundary air pollution data from 33 coastal cities in eastern Asia from January 2015 to July 2017. The results show that our D-CRNN model have achieved 86.2%, 78.6% accuracy of total prediction and transboundary air pollution in next 6 hours..
.

## Slide 5
TITTLE 2: Air Purification System for Street Level Air Pollution and Roadside Air Pollution
AUTHOR: B.Ravi Subrahmanyam1 , Avanish Gautam Dr. Prabhakar Tiwari3
YEAR: 2018
DESCRIPTION:
— Decreasing the pollution level is now the main aim for many. Pollution is in many forms; almost every natural thing is now affected by the term pollution. Not only land, water, air, but each and every thing belongs to the planet is now in danger levels of pollution. Already human civilizations woke up to reduce this danger but are not into many things one of such is air. Air pollution is one of the hardest challenges to the humans as it is beyond our hand limits. So there must be a technology for that to decrease the alarming levels of air pollution. The discussed method also aims to bring the increased levels of pollution back to the bottom. In this method the air is being purified by the use of distilled water only, without the use of any synthetic material and/or chemical substance. Here, the air is made passed through the water so by reaction with water, pollutants stay in it results in clean air. In this method air is being purified by polluting water, but the fact is cleaning water is easy and there are many methods for this but cleaning air needs some boost up in the technology level.

## Slide 6
TITTLE 3: Identifying Outdoor Context by Correlating Air and Noise Pollution Sensor log
AUTHOR: Biswajit Maity , Yashwant Polapragada , Arindam Ghosh , Sanghita Bhattacharjee, Subrata Nandi,
YEAR: 2020
DESCRIPTION:
In an urban area, the degree of ambient noise and air pollution play a vital role in determining the quality of human life. The impact of these two pollutants is increasing day-by-day due to rapid urbanization. Although, creating real-time pollution maps and forecasting of pollution levels have been studied extensively, the contextual, spatio-temporal correlation between air and noise pollution has not been investigated thoroughly. This correlation is important to identify the characteristics of an urban area. In this paper, we have highlighted some aspects that are useful to identify a context from different pollutant data. To collect the noise data, we have developed an android based application ”AudREC” that uses the inbuilt mobile micro-phone sensor. Moreover, for measuring air pollutants, we have used a ready-made ”Flow” device that senses PM2.5 and CO2, etc. The initial outdoor experiments show the feasibility of the platform for recognizing contexts from air and noise pollution information.

## Slide 7
TITTLE 4: Air Pollution Monitoring System using Internet of Vehicles and Pollution Sensors
AUTHOR: Kanpur Rani V, V allikanna A L
YEAR: 2020
DESCRIPTION:
The urban societies are running into fast growth, and an overriding portion of the realms population almost similar to be in built-up societies in the forthcoming generation. Because of the rapid progressions in India, the count of automobiles improved. Besides a few built-up sectors, the automobile count also wrinkled. Motorized automobiles are ace of the primary causes of contamination in the atmosphere. Contamination released from the motorized automobiles is mostly the source of contamination is directly released in the atmosphere as if they occur various biochemical responses amid pollutants it also pollutes the atmosphere this is labeled as secondary pollution. Once the air is infected it is appropriately high, then it grades grave implications, it can even demise the result in a few cases. Additionally, this contamination distresses the public in heart and lung diseases. The work is proposed to monitor the air pollutants in the air and generates the advanced alerts by forecasting the pollution level in the city. It is designed with the various gases that emerge from automobile pollution affecting urban areas. The proposed system has been experimented in a defined environment and it yielded the better performance as 99.23% accuracy to generate the alert for TrueTrue case.

## Slide 8
TITTLE 5: Prediction and Monitoring of Air Pollution Using Internet of Things (IoT)
AUTHOR: Sarita Jiyal ,Rakesh Kumar Saini
YEAR: 2020
DESCRIPTION:
—In all developing countries such as India the main problem of premature death is air pollution which also effect the economy of country. When urbanization started then various problem occurs such as environmental pollution, traffic system etc. there is so much loss of resources in crowded cities due to urbanization. The concept of smart sustainable city can be used to balance the resources. If we do loss of resources excessively than we will definitely create problems to our future generation and excessive use of resources causes air pollution. Than it is necessary to predict air pollution timely by which it can be monitored. Using Internet of Things monitoring of air pollution is necessary to save our environment from all harmful pollutants. Vehicles are the main cause of air pollution. Electric Vehicles and cycles can be used in place of other vehicles for controlling the air pollution. This research teaches that prediction of air pollution level is very important by which peoples can divert there route of travelling.
.

## Slide 9: BLOCK DIAGRAM

## Slide 10: MODULES
Modules Name:
TRANSMITTER
RECEIVER

## Slide 11: TRANSMITTER

## Slide 12
In this module, we get the gases value in the atmosphere using gas sensors series. The MQ-9 (Carbon Monoxide), MQ-135 (Air Quality, CO, Ammonia, Benzene, Alcohol, Smoke), MQ-137(Ammonia), MQ-138(Benzene, Toluene, Alcohol, Acetone, Propane, Formaldehyde gas, Hydrogen)provide the polluted the gas values. After getting the sensors value the LORAtx sends data with GPS to the LORArx. The LCD is used to show the corresponding gases value of the atmosphere.

## Slide 13: RECEIVER

## Slide 14
In this module, the LORArx is used to get the gases value that LORAtx sends the IOT is used update the gases value in a webpage. The GSM is used to send the values of the corresponding location as SMS. The LCD is used to show the gases values

## Slide 15: HARDWARE REQUIREMENTS:
POWER SUPPLY
ARDUINO UNO
LCD
MQ-9
MQ-135
MQ-137
MQ-138
LORA PAIR

## Slide 16: SOFTWARE REQUIREMENTS:
ARDUINO IDE
EMBEDDED C

## Slide 17: ADVANTAGES:
Real time monitoring system
Real time alert system

## Slide 18: APPLICATIONS:
This system is used to monitor the air quality system in the high polluted places to measures the world pollution control.

## Slide 19: FUTURE ENHANCEMENT:
In future we can upgrade the accuracy of the data collecting faster.
We can also get more gases value in future.
.

## Slide 20: CONCLUSION:
The model proposed in this paper serves automatic detection of potholes and humps and alerting vehicle drivers to evade potential accidents. This article reports the development of a novel low-cost sensor node that utilizes cost-effective electrochemical sensors to measure carbon levels. The node can be powered by either solar-recharged battery or mains supply. It is capable of long-range, low power communication over public or private long-range wide area network IoT network and short-range high data rate communication over Wi-Fi. The developed sensor nodes were co-located with an accurate reference CO2 sensor for field calibration.

## Slide 21: REFERENCE:
[1] A. J. Cohen et al., “Estimates and 25-year trends of the global burden of disease attributable to ambient air pollution: An analysis of data from the global burden of diseases study 2015,” Lancet, vol. 389, no. 10082, pp. 1907–1918, May 2017.
[2] N. Castell et al., “Can commercial low-cost sensor platforms contribute to air quality monitoring and exposure estimates?” Environ. Int., vol. 99, pp. 293–302, Feb. 2017.
[3] K. Hu, V. Sivaraman, B. G. Luxan, and A. Rahman, “Design and evaluation of a metropolitan air pollution sensing system,” IEEE Sensors J., vol. 16, no. 5, pp. 1448–1459, Mar. 2016, doi: 10.1109/JSEN.2015.2499308.
[4] B. Maag, Z. Zhou, and L. Thiele, “A survey on sensor calibration in air pollution monitoring deployments,” IEEE Internet Things J., vol. 5, no. 6, pp. 4857–4870, Dec. 2018, doi: 10.1109/JIOT.2018.2853660.
[5] X. Liu, S. Cheng, H. Liu, S. Hu, D. Zhang, and H. Ning, “A survey on gas sensing technology,” Sensors, vol. 12, no. 7, pp. 9635–9665, Jul. 2012.

## Slide 22
[6] Y. Yang, Z. Zheng, K. Bian, L. Song, and Z. Han, “Real-time profiling of fine-grained air quality index distribution using UAV sensing,” IEEE Internet Things J., vol. 5, no. 1, pp. 186–198, Feb. 2018, doi: 10.1109/JIOT.2017.2777820.
[7] M. Chen, J. Yang, L. Hu, M. S. Hossain, and G. Muhammad, “Urban healthcare big data system based on Crowdsourced and cloud-based air quality indicators,” IEEE Commun. Mag., vol. 56, no. 11, pp. 14–20, Nov. 2018.
[8] G. Mois, T. Sanislav, and S. C. Folea, “A cyber-physical system for environmental monitoring,” IEEE Trans. Instrum. Meas., vol. 65, no. 6, pp. 1463–1471, Jun. 2016.
[9] G. Mois, S. Folea, and T. Sanislav, “Analysis of three IoT-based wireless sensors for environmental monitoring,” IEEE Trans. Instrum. Meas., vol. 66, no. 8, pp. 2056–2064, Aug. 2017.
[10] A. Kadri, E. Yaacoub, M. Mushtaha, and A. Abu-Dayya, “Wireless sensor network for real-time air pollution monitoring,” in Proc. 1st Int. Conf. Commun., Signal Process., Their Appl. (ICCSPA), Feb. 2013, pp. 1–5.

## Slide 23: THANK YOU